## Slide 1
Literature Review & Emerging Trends
Industrial Wireless Communication for Industry 4.0

## Slide 2
2.1 Early Wireless Sensor Networks (WSN)
Foundation
WSN established the foundation of industrial wireless communication, based on IEEE 802.15.4 standards.
Main Goal
Collect and transmit data wirelessly with low power consumption, allowing devices to run on batteries for years.
Key Challenges
Unstable delays, electromagnetic interference from machines, and signal loss in metallic factory environments.
Significance
Despite the challenges, WSN shaped the design principles still used in modern industrial wireless systems today.

## Slide 3
2.2 Industrial Wi-Fi Evolution
802.11b/g
High variable latency — not suitable for closed-loop industrial control.
802.11e
QoS (EDCA) introduced traffic prioritisation, improving reliability.
802.11n
MIMO antennas enabled spatial multiplexing and increased data rates.
Wi-Fi 6
OFDMA and TWT reduced latency to ~5 ms — suitable for high-bandwidth industrial applications.

## Slide 4
2.3 5G and the URLLC Paradigm
< 1 ms
Latency for motion control
99.9999%
Reliability (URLLC)
70%+
New private wireless spend on standalone 5G (2025)
• 3GPP Release 15 (2018): 5G NR air interface standardised.
• Release 16 (2020): mini-slot scheduling and enhanced HARQ added for URLLC.
• Release 16 also defines 5G as a TSN bridge for end-to-end deterministic delivery.
• Many industries are now adopting private 5G networks for real-time control tasks.

## Slide 5
2.4 TSN Integration — Towards Wireless Determinism
What TSN Provides
• Credit-Based Shaping (802.1Qav)
• Time-Aware Shaping (802.1Qbv)
• Cyclic Queuing and Forwarding (802.1Qch)
• Sub-microsecond time synchronisation
Key Impact
• Wireless becomes as reliable as wired PROFINET / EtherCAT.
• Wired and wireless robot axes driven by the same scheduler.
• IEEE actively extending TSN standards to Wi-Fi (802.11).

## Slide 6
Emerging Trends
Wi-Fi 7 · Private 5G · Wireless TSN · 6G Outlook

## Slide 7
5.1 Wi-Fi 7 — Multi-Link Operation (MLO)
2.4 GHz
5 GHz
6 GHz
All three frequency bands used simultaneously
• MLO provides packet-level diversity — a dropped packet on one band is recovered on another without retransmission delay.
• IEEE 802.11be (Wi-Fi 7) is finalised. Draft 1.0 of Wi-Fi 8 (802.11bn) completed August 2025.
• Wi-Fi 8 targets deterministic performance and reliability rather than just higher throughput.

## Slide 8
5.2 Private 5G Campus Networks
of new private wireless
spend in 2025
• Companies build and manage their own 5G network instead of using public infrastructure.
• Full control over security, service levels, and spectrum allocation.
• Optimised for deterministic, high-density industrial environments such as factories.
• Complements industrial Ethernet and Wi-Fi in new (greenfield) factory deployments.

## Slide 9
5.3 Wireless Time-Sensitive Networking
• TSN ensures data arrives at the exact required time — critical for real-time control.
• Closes the "last mile" gap: wireless now matches wired PROFINET and EtherCAT guarantees.
• A single TSN scheduler can drive both wired and wireless robot axes at the same time.

## Slide 10
Wireless Standards: Architecture and Protocol Stack
Wi-Fi (802.11) · Zigbee (802.15.4) · 5G New Radio

## Slide 11
3.1 IEEE 802.11 (Wi-Fi)
Operates on 2.4, 5 and 6 GHz bands
CSMA/CA for channel access
Wi-Fi 6 adds OFDMA and TWT
802.11r enables fast roaming for AGVs
Throughput up to 9.6 Gbps
PROS
High speed, huge ecosystem, native TCP/IP
CONS
Unreliable under load, shared spectrum
[ IMAGE ]
Wi-Fi factory deployment

## Slide 12
3.2 IEEE 802.15.4 / Zigbee
Low-power wireless WPAN standard
Runs at 2.4 GHz, up to 250 kbps
Three roles: Coordinator, Router, End Device
Supports star, tree and mesh topologies
Battery life of 2 to 5 years
PROS
Long battery life, low cost, self-healing mesh
CONS
Low data rate, short range of 10 to 100 m
[ IMAGE ]
Zigbee mesh topology

## Slide 13
3.3 5G New Radio (NR)
Standardised by 3GPP, uses licensed bands
Three classes: eMBB, mMTC, URLLC
URLLC reaches under 1 ms at 99.999%
Private campus networks kept on site
Acts as a TSN bridge from Release 16
PROS
Licensed spectrum, deterministic, private networks
CONS
Costly, complex, power-hungry
[ IMAGE ]
Private 5G campus network

## Slide 14
3.4 Standards at a Glance
 | Wi-Fi | Zigbee | 5G NR
Data rate | 9.6 Gbps | 250 kbps | Multi-Gbps
Latency | ~5 ms | 15 to 30 ms | < 1 ms
Range | ~100 m | 10 to 100 m | Wide / campus
Power use | High | Very low | High
Best for | High bandwidth | Sensors | Real-time control
Takeaway: no single standard fits every need, so factories mix all three by use case.